## Slide 1: Universal Serial Bus (USB)
CSE 315
Peripheral and Interfacing
Md Mahedi Hassan
Lecturer, Dept. of CSE, UAP

## Slide 2: Introduction
A plug and play interface that allows a computer to communicate with peripheral and other devices
A fast, bidirectional, isochronous, low-cost, dynamically attachable/detachable serial interface for connecting peripherals.

## Slide 3: Features
Simplifies connection process and enables addition of peripherals
Establishes communication over a 4-wire cable
Supported data transfer rates
  480Mb/s
  12Mb/s
  1.5Mb/s
Many peripherals over one port
Up to 127 peripherals can be connected to a OC

## Slide 4: Features (Cont…)
Bandwidth share using token-based protocol
Conforms plug and play
Distributes electrical power automatically
Allows two-way data flow
Replaces serial and parallel port
Windows 98 and Windows NT have USB support

## Slide 5: USB System
USB Host refers to a PC
Only one USB Host allowed in the system
USB Device refers to Peripheral Devices
USB Host
USB Device
USB Cable

## Slide 6: USB Cable
Four wires
  D+ and D- data lines carry signals between host and device
  VBUS and GND delivers power
Allows supply voltage to be between 5.25V and 4.2V

## Slide 7: USB Connector
Two types of connectors
  Type A (for PC)
  Type B (for peripherals)

## Slide 8: Implementation of USB Interface
Client Software
USB System Software
USB Host Controller
Function
USB Logical Device
USB Bus Interface
USB Interconnect
HOST
DEVICE

## Slide 9: USB Host
Detects attachment and removal of USB devices
Manages flow of control information
Manages flow of data
Collects activity and status information of USB devices
Provides power to low power devices

## Slide 10: USB Device
Monitors device address in each communication and selects itself
Responds to all requests made by host
Adds error checking bits and checks for errors
Manages its own power supply

## Slide 11: USB Device (Cont…)
Custom I/O device
Protocol controller Application firmware
Transceiver
Serial Inference Engine
Bus interface H/W
Real world I/O
byte
control
D+
D-

## Slide 12: USB Device (Cont…)
Serial Inference Engine (SIE) has a buffer of definite size known as end points
  It stores configuration and data information
  Host delivers data into OUT end point
  Device places data into IN end point
  A device has up to 16 IN and 16 OUT end points
Transceiver takes care of the electrical requirements
SIE takes care of the bit timing
USB device controller (a microprocessor/microcontroller/digital signal processor) executes a program to respond to various requests

## Slide 13: Transfer Types
Four basic types of data transfer between the host and the devices
  Control transfer
  Bulk data transfer
  Interrupt data transfer
  Isochronous data transfer

## Slide 14: Control Transfer
Configures a device at attach time
High priority
Automatic error protection
High data rate

## Slide 15: Bulk Data Transfer
Used to transfer bulk amount of data to a printer or from a scanner
Time is not a critical parameter
Implements error detection in hardware
Sequential data transfer

## Slide 16: Interrupt Data Transfer
Timely but reliable data transfer
Interrupt data are
  Event notifications
  Characters
  Coordinates
Keyboards and mouse use this method

## Slide 17: Isochronous Data Transfer
Streams real time data transfer
Devices transferring huge amount of data at definite rate use this method (Example: sound cards)
Does not implement error detection

## Slide 18
THANK YOU