## Slide 1
7 Segment Display
CSE 315
Peripherals & Interfacing
Md Mahedi Hassan
Lecturer, CSE, UAP

## Slide 2
Agenda
Today We'll learn about 7 segment display and it's arduino usage

## Slide 3
An LED or Light Emitting Diode, is a solid state optical pn-junction diode which emits light energy in the form of photon. The main advantage of light emitting diodes is that because of their small die size, several of them can be connected together within one small and compact package producing what is generally called a 7-segment Display.
What is 7 segment display?

## Slide 4
Why 7 Segment?

## Slide 5: Types of 7 Segment display
The Common Cathode (CC) – In the common cathode display, all the cathode connections of the LED segments are joined together to logic “0” or ground. The individual segments are illuminated by application of a “HIGH”, or logic “1” signal via a current limiting resistor to forward bias the individual Anode terminals (a-g).

## Slide 6: Types of 7 segment display (contd.)
The Common Anode (CA) – In the common anode display, all the anode connections of the LED segments are joined together to logic “1”. The individual segments are illuminated by applying a ground, logic “0” or “LOW” signal via a suitable current limiting resistor to the Cathode of the particular segment (a-g).

## Slide 7
Truth Table of 7 segment
Here "x" means switch is closed/connected so that current can pass through that pin

## Slide 8
Some Use Case
Counter
Speed measuring device
Digital Clock
Cashier machine
Digital meter
Microwave oven
Washing machine

## Slide 9
4 Digit 7 Segment Display

## Slide 10: Pin Configuration

## Slide 11: How it works
Using all digits simultaneously would require 32 pins
One digit is activated at a time through its own selection line
The trick is to activate one display at a time, continuously, in a very fast manner
This will make the human eye see all the digits turned on

## Slide 12: Thank you!
Thank you!